## Slide 1: HackEDbeta 2024 Introduction to the Raspberry Pi Pico
Steven Knudsen, PhD PEng
knud@ualberta.ca

## Slide 3: Outline
Raspberry Pi Pico and Pico W overview
Setting up for MicroPython
Setting up for C/C++
What about Rust?
Wokwi.com and Pico

## Slide 4: Sources for the talk
github.com/StevenKnudsen/HackEDbeta2024Workshop

## Slide 5: Assumptions
You know how to program in at least one of the languages
  Python or C
You have a Pico
  You have two if you want to program in Rust

## Slide 6: Raspberry Pi Pico and Pico W
Raspberry Pi Pico is a low-cost, high-performance microcontroller board with flexible digital interfaces. Key features include:
RP2040 microcontroller chip designed by Raspberry Pi in the United Kingdom
Dual-core Arm Cortex M0+ processor, flexible clock running up to 133 MHz
264 kB of SRAM, and 2MB of on-board flash memory
USB 1.1 with device and host support
Low-power sleep and dormant modes
Drag-and-drop programming using mass storage over USB
26 × multi-function GPIO pins
2 × SPI, 2 × I2C, 2 × UART, 3 × 12-bit ADC, 16 × controllable PWM channels
Accurate clock and timer on-chip
Temperature sensor
Accelerated floating-point libraries on-chip
8 × Programmable I/O (PIO) state machines for custom peripheral support
Images from digikey.ca

## Slide 7: Raspberry Pi Pico and Pico W
Images from digikey.ca
$CA5.80 at Mouser.ca $CA8.34 at canada.newark.com

## Slide 8: Getting started with the Pico - MicroPython
The main reference is a very good tutorial
https://projects.raspberrypi.org/en/projects/getting-started-with-the-pico/0

## Slide 9: Pico on breadboard
https://projects.raspberrypi.org/en/projects/getting-started-with-the-pico/1

## Slide 10: RPi Pico Pins

## Slide 11: Install Thonny (Win/Lin/macOS)
Notes: This is Thonny, a beginner Python IDE. Happens to be running on a MacBook Pro, but same for other OSes

## Slide 12: Pico in boot select (bootsel) mode
Unplug Pico from USB
Press and hold bootsel button
Plug Pico into USB and wait a few seconds
Release bootsel button
Open Thonny
https://projects.raspberrypi.org/en/projects/getting-started-with-the-pico/3

## Slide 13: Install MicroPython
Notes: Open the hamburger menu in the lower right corner and select install micropython

## Slide 14: Install dialogue
Notes: The RPi will disconnect when this is done, then reconnect

## Slide 15: Connect
Notes: We need to connect to the Pico. Again, open the hamburger menu. Notice these are both really the same, so it doesn’t matter which we choose.

## Slide 17: Success!

## Slide 18: GPIOs
Lots of support for GPIO and other peripherals at MicroPython.org
Quick Reference for MicroPython is found at
https://docs.micropython.org/en/latest/rp2/quickref.html
Support for
HW Timers, GPIO, UART, PWM, ADC, SW SPI, HW SPI, SW I2C, HW I2C, I2S, RTC, WDT, OneWire, NeoPixel, APA106
… but probably not …

## Slide 19
monkeyuser.com

## Slide 20: Simple RGB blinky

## Slide 21: Live demo

## Slide 22: Getting started with the Pico - C/C++
The main reference is the RPi documentation
https://www.raspberrypi.com/documentation/microcontrollers/c_sdk.html
As per that page there are on Github an SDK and Examples repos
Will use Ubuntu 24.04 for the following, but instructions for Win and macOS are on the link above
(Could set up development on a Raspberry Pi, but we won’t for HackEDxx)

## Slide 23: Toolchain and SDK install
Need cmake and the GCC ARM toolchain
Make a top-level directory in my Development directory to clone the SDK into
Clone the Pico examples
sudo apt install cmake gcc-arm-none-eabi libnewlib-arm-none-eabi libstdc++-arm-none-eabi-newlib
cd ~Development
mkdir RPi; cd RPi
git clone https://github.com/raspberrypi/pico-sdk.git
git clone https://github.com/raspberrypi/pico-examples.git

## Slide 24: Follow the Getting Started
Follow the Getting Started Guide…
Do the “blink” example to be sure the tool chain is up and running.
For this example I use an RP2040 board from Universal Solder.
Pressing BOOTSEL while plugging it in results in it looking like a storage device. Programming is drag’n’drop
Different Pico
From Universal Solder

## Slide 25: Blink example
Let’s make sure the blink example works
The build will take a long time since all the examples will be compiled…
cd ~Development/RPi/pico-examples
mkdir build; cd build
cmake ..
make –j4

## Slide 26: Blink example
When complete, connect power to the Pico while holding the boot select button. The Pico will mount as a storage device. Drag and drop ~Development/RPi/pico-examples/build/blink/blink.uf2 onto the Pico
The blue LED should blink

## Slide 27: Replicate previous MicroPython Example
The main steps to make a custom C/C++ application are
In pico-examples copy blink folder and contents
Rename blink.c to rgb_demo.c and edit the CMakeLists.txt file replacing blink with rgb_demo
cd ~/Development/RPi/pico-examples cp -dpR blink rgb_demo
cd rgb_demo

## Slide 28: Replicate previous MicroPython Example cont’d
In the pico-examples directory, edit the CMakeLists.txt file
  Find where the blink example is added
  Replicate those lines and replace blink with rgb_demo
Change directory in to the build directory and execute cmake ..
There should be a new directory named rgb_demo. Change directory into it and execute
make -j4
There should be a new executable named rgb_demo.
Put the Pico back into bootloader mode and drop the rgb_demo.uf2 file on the drive – the old blink demo should work

## Slide 29
Let’s replace the rgb_demo.c source with the equivalent of the python
#include "pico/stdlib.h"
#include "hardware/gpio.h"
const uint8_t RGB_PIN1 = 0;
const uint8_t RGB_PIN2 = 1;
const uint8_t RGB_PIN3 = 2;
int main() {
gpio_init(RGB_PIN1);
gpio_set_dir(RGB_PIN1, GPIO_OUT);
gpio_init(RGB_PIN2);
gpio_set_dir(RGB_PIN2, GPIO_OUT);
gpio_init(RGB_PIN3);
gpio_set_dir(RGB_PIN3, GPIO_OUT);
while (true) {
gpio_put(RGB_PIN1, 0);
gpio_put(RGB_PIN2, 1);
gpio_put(RGB_PIN3, 1);
sleep_ms(250);
gpio_put(RGB_PIN1, 1);
gpio_put(RGB_PIN2, 0);
gpio_put(RGB_PIN3, 1);
sleep_ms(250);
gpio_put(RGB_PIN1, 1);
gpio_put(RGB_PIN2, 1);
gpio_put(RGB_PIN3, 0);
sleep_ms(250);
}
}

## Slide 30: GOTCHA!

## Slide 31
NOT THE SAME!

## Slide 32: Live demo

## Slide 33: What about Rust
Doable
However, we don’t have time today to go through all the steps, it’s involved!
https://reltech.substack.com/p/getting-started-with-rust-on-a-raspberry
Happy to help you if you need it for HackEDbeta

## Slide 34: One more tool – Wokwi.com

## Slide 36: What is Wokwi.com? (from docs.wokwi.com)
Wokwi is an online Electronics simulator. You can use it to simulate Arduino, ESP32, STM32, and many other popular boards, parts and sensors.
Here are some quick examples of things you can make with Wokwi:
Arduino Uno "Hello World"
Blink an LED on ESP32
Monitor the weather on ATtiny85
Control 32 Servos with Arduino Mega
Animate an LED Matrix with FastLED
7 Segment Counter with MicroPython on ESP32
…and Pico!

## Slide 38: Simple RGB blinky

## Slide 39: Wokwi Version

## Slide 40: Trivia
...with wee prizes...

## Slide 41: Trivia
Who created the first artificial neural network and when?

## Slide 42
Warren McCulloch and Walter Pitts
1943
Perceptron
Modelled using electrical circuits
Notes: Prize 1 chosen

## Slide 43: Trivia
What is an equivalent to the U of A’s main frame computer from the 80s?

## Slide 44: Amdahl 470 v/6
Date Introduced : 1975
Dimensions overall: 63” x 70” x 26”
Keywords : Clones; Plug compat; IBM
Speed : 3.5 MIPS
Memory Size : up to 8MB
Memory Width : 32-bit
Cost : $3,750,000 (2020 $17,981,250)

## Slide 45: Arduino
Date Introduced : 2010
Dimensions overall: 2.7” x 2.1” x 0.6”
Speed : 8 - 11 MIPS
Memory Size : 32k FLASH 2k SRAM
Cost : ~$20
Cost to make : < $5

## Slide 46: Trivia
What are the most loved and hated languages in the 2022 Dice survey
Notes: https://www.dice.com/career-advice/20-programming-languages-that-developers-love-the-most

## Slide 47: Most loved
Rust 86.83%
Elixir 75.46%
Clojure 75.23%
TypeScript 73.46%
Julia 72.51%
Python 67.34%

## Slide 48: Most hated
VBA (78.56 percent).
COBOL (hated by 79.96 percent of developers)
MATLAB (80.84 percent), and

## Slide 49: Most hated
VBA (78.56 percent).
COBOL (hated by 79.96 percent of developers)
MATLAB (80.84 percent), and